MK. II CARGO ROBOT
USER'S MANUAL

FOR INDOOR USE ONLY

DO NOT DRIVE ROBOT INTO PEOPLE – INJURY MAY OCCUR

AVOID DRIVING ROBOTS INTO WALLS, APPLIANCES, ETC. – DAMAGE MAY OCCUR

MAIN ASSEMBLIES

- Roku Camera: It provides a live video stream for remote operation. Any device that supports a Roku Camera or Smart Home app can be used to view the live video stream, e.g. Roku TV, iPad, and Android or iOS phone.
- Basket: It carries cargo. The handles may be used to lift the robot. Avoid placing items in the basket that block the camera.
- Tower: It has the camera, motor controllers, and remote control receiver. A clear back panel provides a view of status LEDs on the remote control receiver and motor controllers.
- Battery box: It is on the bottom of the robot. It has a power switch, power indicator LED, and battery charging jack on the outer right side. Inside, there is a 7.2V 5000mAH NiMH battery pack and a fuse box that distributes power. It uses four automotive blade type fuses. There is a 5A fuse for each motor, the camera, and the power indicator LED.
- Drive train: It has the two motors, drive wheels, and anti-tip skids.
- Caster: It is a dual-wheel furniture caster with a mounting blocks and spacers.
- Hand-held remote: It is used to drive the robot.

POWER

A three-position switch controls power to the robot.

- Flip the power switch up to “power up” the robot.
- Flip the power switch down to “power down” the robot.
- The power indicator LED by the switch turns on when the switch is in the up position.
- Use the down position for charging.
- The middle position disables charging and normal operation.
If the robot is out of control, grab it and/or tip it on its back, and flip the switch.

Press and hold the “ON” button to toggle power on the hand-held remote. The green LED on the remote control receiver will be solid when the hand-held remote is on and a link is established. It will blink if the hand-held remote is off or no link is established.

DRIVING

The robot uses “tank” steering.

- Move joystick forward to go forward.
- Move joystick backward to go backward.
- Move joystick left or right to spin in place.
- Move joystick left/right while also moving it forward/backward to turn.

Auto-throttle mode:

- Click the OK button on front of the transmitter. Listen for one beep.
- Push the joystick forward and release it again. Listen for one beep.
- Repeat push-forward-and-release on the joystick until robot starts moving.
- Additional push-forward-and-release will increase speed.
- Move joystick left or right to steer.
- Click the OK button on front of the transmitter to exit auto-throttle mode.

CHARGING

The robot and the hand-held remote are rechargeable. To recharge the robot:

- Put the power switch in the down position.
- Pull out the plastic plug that protects the charging connector.
- Plug the charger jack into the robot.
- Plug the charger into a wall socket.
- The charger's LED will be red while the unit is charging.
- The charger's LED will be green when charging is complete.
- Unplug the charger jack from the robot.
- Unplug the charger from the wall.
- Replace the plastic plug that protects the charging connector.

It may take several hours to charge the battery.

Do not leave the robot unattended while charging.

Do not leave the charger connected after the battery is fully charged.

Any 5V phone charger with a USB-C plug can charge the hand-held remote. A red light by the joystick turns on when the unit is charging. A small green light turns on near the USB-C plug when charging is complete.

RECONFIGURING CAMERA

The robot uses a stock Roku camera. It will need to be reconfigured when the robot is moved to a location with a different WiFi network.

- Gently tilt the back of the camera up.
- Gently tilt the front of the camera up.
- The camera configuration buttons are under the front of the camera near the lens.
- Follow instructions for configuring Roku camera.
- Gently press the camera back into place.

Use a Roku camera app to disable all notifications and event detection features. Driving the robot can generate unwanted events. Additional camera features configurable by the app include:

- Night vision mode
- 2-way audio
- Siren

REPLACING CAMERA

The camera can be removed and replaced if desired.

- Remove the four screws on the sides of the tower that secure the clear back panel.
- Use the yellow velcro tabs to grab the back panel and remove it.
- Unplug the white camera power cable (micro USB).
- Push the cable connected to the camera up through the hole in the tower.
- Slide the camera forward. Do NOT pull up on the camera.

Reverse the process to replace the camera.

REGUALAR MAINTENANCE

- Inspect fasteners. Tighten any that are loose. Do not over-tighten. Tools required:
  - Various Phillips-head screwdrivers (body and some motor mount screws)
  - Small flathead screwdriver (camera mount)
  - 7/64” hex key (for wheel mount hardware)
  - 3mm hex key (for motor mount hardware)
- Inspect wiring. If anything appears to be broken, do not use the robot. Contact builder.
- Remove any debris from wheels or axles that may interfere with movement.

TROUBLESHOOTING

PROBLEM	SOLUTION
Nothing happens when power is turned on.	Battery might be completely dead. Charge battery. / Internal wiring might be broken. Contact builder.
Main power light doesn't work but receiver blinks.	Fuse might be blown. Check fuses. / Internal wiring might be broken. Contact builder.
One motor stopped working.	Fuse might be blown. Check fuses. / Internal wiring might be broken. Contact builder.
Both motors stopped working.	Battery might be low. Charge battery. / Fuses might be blown. Check fuses. / Internal wiring might be broken. Contact builder.
Both motors work but inputs from transmitter do not produce desired movement.	Motors might be out of trim. Adjust trim controls on transmitter. / Transmitter might be configured incorrectly. Reconfigure transmitter for “hybrid” mode. / Motors might be connected incorrectly. Contact builder. / Motor controllers might be connected incorrectly. Contact builder.
Receiver blinks but does not respond to transmitter.	Transmitter battery might be dead. Charge transmitter. / Transmitter and Receiver link might not be configured. Follow manual to reconfigure link.
Camera doesn't work (no LED lights).	Battery might be low. Charge battery. / Fuse might be blown. Check fuses. / Internal wiring might be broken. Contact builder.
Camera doesn't work (can't connect with viewing device).	Link might be configured incorrectly. Reconfigure Roku camera. / If red LED is blinking, the camera might be getting an automatic update. Leave camera on for several minutes. Cycle power and try connecting again.
Run time is shorter than expected after full charge.	Battery may be faulty. Replace battery.